## Slide 1
Jennifer Zhang, Gilla Wu, Rebecca Shih, Pranav Piedy, Nuoci Ding
Why Flight Pairing Matters?
Delays don’t stay isolated — they spread
Pilot sequences connect multiple flights
Weather risk varies by airport and season
High-risk inbound + outbound = fragile schedule
Operational Resilience: Identifying Pilot Sequence Disruptions

## Slide 2
Key Data Sources
Together, these sources help us with relevant data to model and penalize high-risk flight pairings.
BTS Data On-Time Performance
Foundation of pilot sequencing. Identifies tight connections & unpredictable inbound flights.
FAA ASPM Performance Metrics
Congestion increases delay risk. We avoid pairings passing through peak congestion.
Weather AWC / NOAA
Volatile weather causes disruption. We avoid pairings with simultaneous weather risks.
Internal Staffing Pilot Schedules
Accounts for operational & fatigue risk using strict airline-specific scheduling rules.
WHAT IT PROVIDES
• Arrival and departure delays. • By route, airport, and time/date.
HOW WE USE IT
• Turn buffer • Arrival variability
WHAT IT PROVIDES
• Flight schedules/delays. • Airport, city-pair (route) and taxi time.
HOW WE USE IT
• Congestion patterns • Congestion vs. delays relationship
WHAT IT PROVIDES
• METAR, TAF. • Historical seasonal and weather patterns.
HOW WE USE IT
• Identify seasonal trends • Predict volatility
WHAT IT PROVIDES
• Existing sequences, pilot times, rules, crew base.
HOW WE USE IT
• Calculate duty length • Check limit violations
IMPORTANCE
IMPORTANCE
IMPORTANCE
IMPORTANCE

## Slide 3
Feature Engineering:
Decoding Sequence Vulnerability
From single-flight metrics → sequence fragility
1. Node Risk — Individual Airports
2. Edge Risk — Pairwise Connection
3. Hub Buffer — DFW Context
•
Seasonal weather sensitivity (impact differs by season)
•
Same weather ≠ same delay (airport-specific response)
•
Arrival vs. departure recovery (how fast delays clear)
•
Delay amplification (30 min → 60min)
Weather correlation (shared storm systems)
Seasonal co-risk (both risky at once)
•
•
•
Turnaround slack
•
Peak bank window
•
Congestion multiplier

## Slide 4
Historical Flight Data (Latency Patterns)
Model Approach
Crew Rules (Union/FAA)
Combined Risk Probabilities & Network Embeddings
Real-Time Weather (Sparse Event Data)
Operational Constraints (Aircraft/Gate)
Disruption-Ready Reserves Strategic Buffer Allocation
Optimized Rosters Push via API
Live Manager Dashboard Real-time KPI Monitoring
Model A: Spatio-Temporal GNN
Model B: XGBoost Classifier
HARD CONSTRAINTS
SOFT OBJECTIVES
▪
Union CBA & FAA Legalities
▪
Aircraft Type-Rating Compatibility
▪
Minimum Connection Times (MCT)
▪
Base Return Requirements
▪
Minimize Premium Pay & Deadhead Costs
▪
Maximize Sequence Robustness Score
▪
Optimize Crew Quality of Life (QoL) Metrics
LAYER 1: DATA INGESTION
LAYER 2: INTELLIGENCE ENGINE
LAYER 3: SOLVER (SIP CORE)
LAYER 4: EXECUTION INTERFACES
SIP ENGINE

## Slide 5
Evaluation: Measuring Real Operational Impact
Why Accuracy Is Not Enough
Key Success Metrics
Severe disruptions are rare but extremely costly. A model could be 99% accurate by simply predicting "no delay" every time.
Missing a few critical cases causes most of the damage. We must prioritize catching the failures.
Success means preventing the few failures that cause the most disruption.
Ranking Quality - Precision @ K
Are the “top ranked flight pairs” the one’s that actually break the schedule?
System Impact - Reduction in Downstream Delay
Do delays stop propagating along legs?
Operational Failure
Missed connection rate
Crew Duty Risk Proxies
Tight turnaround failures

## Slide 6
From Risk Scores to Scheduling Decisions
Deployment Philosophy
How the Output Is Used
Option 1: Do-Not-Pair List Hard exclusions for consistently high-risk flight pairings
Option 2: Penalty-Based Optimization Risk scores enter crew pairing as soft costs
Business Impact
•
Decision support, not automation
•
Does not replace crew scheduling systems
•
Fewer cascading delays
•
Lower recovery costs
•
More resilient schedules under stress

## Slide 7
Thank You